## Slide 1: Sequential Circuit Design

## Slide 2: State Optimization
Equivalent States:
  Two states are equivalent if, for each member of the set of inputs,
    they give exactly the same output and
    send the circuit either to the same state or to an equivalent state.
  If two states are equivalent, one can be eliminated without effecting the behavior of the FSM.

## Slide 3: State Optimization Algorithm: Row Matching
  Two states are equivalent if any of the conditions are true:
    If two states have the same output AND both transition are to the same next state,
    If two states have the same output AND both transition are to each other
    If two states have the same output AND both self-loop.
  Combine the equivalent states into a new renamed state.
  Repeat until no more states are combined.

## Slide 4: Row Matching Example
NS output
PS x=0 x=1 x=0 x=1
a a b 0 0
b c d 0 0
c a d 0 0
d e f 0 1
e a f 0 1
f g f 0 1
g a f 0 1
State Transition Table

## Slide 5: Row Matching Example (cont)
NS output
PS x=0 x=1 x=0 x=1
a a b 0 0
b c d 0 0
c a d 0 0
d e f 0 1
e a f 0 1
f e f 0 1
NS output
PS x=0 x=1 x=0 x=1
a a b 0 0
b c d 0 0
c a d 0 0
d e d 0 1
e a d 0 1
Reduced State Transition Diagram

## Slide 6: State Optimization Algorithm
Implication Chart
Present State | Next State |  | Present Output
 | X=0 | 1 | X=0
a | d | c | 0
b | f | h | 0
c | e | d | 1
d | a | e | 0
e | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1

## Slide 7: State Optimization Algorithm
Implication Chart After First Pass
  Processing order is important

## Slide 8: State Optimization Algorithm
Implication Chart After Second Pass
Present State | Next State |  | Output
 | X=0 | 1 | 
a | a | c | 0
b | f | h | 0
c | c | a | 1
f | f | b | 1
g | b | h | 0
h | c | g | 1

## Slide 9: Equivalent Sequential Circuits
Definition:
  Sequential circuit N1 is equivalent to sequential circuit N2 if
    for each state p in N1, there is a state q in N2 such that p≡q , and
    conversely, for each state s in N2 , there is a state t in N1 such that s≡t.

## Slide 10: Example
 | X=0 | X=1 | X=0 | X=1
A | B | A | 0 | 0
B | C | D | 0 | 1
C | A | C | 0 | 1
D | C | B | 0 | 0
 | X=0 | X=1 | X=0 | X=1
S0 | S3 | S1 | 0 | 1
S1 | S3 | S0 | 0 | 0
S2 | S0 | S2 | 0 | 0
S3 | S2 | S3 | 0 | 1

## Slide 11
Implication Tables:
 | X=0 | X=1 | X=0 | X=1
A | B | A | 0 | 0
B | C | D | 0 | 1
C | A | C | 0 | 1
D | C | B | 0 | 0
 | X=0 | X=1 | X=0 | X=1
S0 | S3 | S1 | 0 | 1
S1 | S3 | S0 | 0 | 0
S2 | S0 | S2 | 0 | 0
S3 | S2 | S3 | 0 | 1

## Slide 12: State Encoding
  The simplest assignment of s coded states to 2n possible states is to use the first s binary integers in binary counting order.
    000, 001, 010, 011, 100
  However, the simplest state assignment does not always lead to the simplest circuit.
    In fact, the state assignment often has a major effect on circuit cost (was previously shown).
  In general, the only formal way to find the best assignment is to try all the assignments.
    That’s too much work!!

## Slide 13: Example
  Design a clocked synchronous state machine with two inputs, A and B, and a single output Z that is 1 if:
    – A had the same value at each of the two previous clock ticks, or
    – B has been 1 since the last time that the first condition was true.
    – Otherwise, the output should be 0.
A
B
Z

## Slide 14: Timing Diagram

## Slide 15: Moore Machine
Reset/0
00
init
A0
A0: got 0 on A
01
10
A1
11
00
01
01
A1: got 1 on A
OK00
OK11
10
11
OK00: got 00 on A
OK11: got 11 on A
10
11
00
10
00
01
00
01
10
11
OKA0
OKA1
11
10
11
00
01
11
01
10
00
OKA0: still OK (because from an OK state, got B=1), and got a 0 on A
OKA1: still OK (because from an OK state, got B=1), and got a 1 on A

## Slide 16: State Table
  OK00 and OKA0 are equivalent
  OK11 and OKA1 are equivalent

## Slide 17: Moore Machine
Reset/0
00
init
A0
A0: got 0 on A
01
10
A1
11
00/01
A1: got 1 on A
OK0
OK1
10
11
OK00: got 00 on A
OK11: got 11 on A
10
11
00
10
00
01
00
01
10
11
OKA0: still OK (because from an OK state, got B=1), and got a 0 on A
OKA1: still OK (because from an OK state, got B=1), and got a 1 on A
01
11
11

## Slide 18: State Encoding
Guidelines:
  Choose an initial coded state into which the machine can easily be forced at reset
    00. . . 00 or 11. . . 11 in typical circuits.
  Minimize the number of state variables that change on each transition.
  Maximize the number of state variables that don’t change in a group of related states
    i.e., a group of states in which most of transitions stay in the group.

## Slide 19: State Encoding
Samples:

## Slide 20: Synthesis Using D FF
Present State
Next State
Output

## Slide 21: State Assignment
Unused States:
  Each of the m states must be assigned a unique code
  Minimum number of bits required is n such that n ≥ log2 m where x is the smallest integer ≥ x
  There are 2n - m unused states

## Slide 22: State Assignment
Unused States:
  Minimal risk:
    Assumes: FSM may get into unused (or “illegal”) states,
      Due to a hardware failure, an unexpected input
     Unused states go to the “initial” state (or a legal state)
  Minimal cost:
    Assumes: FSM never enters an unused state
     Next-state entries of the unused states can be marked as “don’t-cares”.

## Slide 23
Reset/0
00
init
A0
01
10
A1
11
00/01
OK0
OK1
10
11
10
11
00
10
00
01
00
01
10
11
01
11
11
Present State
Next State

## Slide 24: Case 1: Minimal Risk
Assumption:
  Unused states go to 000 (minimal risk)
D1 = Q1 + Q2¢.Q3¢

## Slide 25: Case 1: D2 Equation
D2 = Q1.Q3¢.A¢ + Q1.Q3.A + Q1.Q2.B

## Slide 26: Case 1: D3 Equation
D3 = Q1.A + Q2¢.Q3¢.A

## Slide 27: Case 1: Z Equation
Z = Q1.Q2.Q3¢ + Q1.Q2.Q3
= Q1.Q2

## Slide 28: Case 2: Minimal Cost
Assumption:
  next states of unused states are “don’t-cares” (minimal cost).
   Z = don’t care for unused states.
D1 = 1

## Slide 29: Case 2: D2 Equation
D2 = Q1.Q3¢.A¢ + Q3.A + Q2.B

## Slide 30: Case 2: D3 Equation
D3 = A

## Slide 31: Case 2: Z Equation
Z = Q2

## Slide 32: Case 2: Logic Diagram

## Slide 33: Third Solution
Trade-off:
  Use minimal cost.
  Then check to see if there is serious problem.
  Incrementally modify.

## Slide 34: Case 3: Synthesis Using JK FF
0
0
1
1
No change
Set
Reset
Complement
Operation
J
0
1
0
1
K
0
1
Q(t+1)
Q(t)
Q(t)
Q(t+1)
0
1
1
0
Q(t)
0
0
1
1
Operation
X
X
0
1
K
0
1
X
X
J
No change
Set
Reset
No Change
Characteristic Table:
Excitation Table:

## Slide 36: Case 3: Synthesis Using JK FF
  Needs separate logic for J and K.
J1 = Q2¢.Q3¢

## Slide 37: Case 3: Synthesis Using JK FF
K1 = 0

## Slide 38: Case 3: Synthesis Using JK FF
J2 = Q1.Q3¢.A¢ + Q1.Q3.A

## Slide 39: Case 3: Synthesis Using JK FF
K2 = Q1¢ + Q3¢.A.B¢ + Q3.A¢.B¢

## Slide 40: Case 3: Synthesis Using JK FF
J3 = Q2¢.A + Q1.A

## Slide 41: Case 3: Synthesis Using JK FF
K3 = Q1¢ + A¢

## Slide 42: Case 3: Synthesis Using JK FF
  These equations take two more gates to realize than minimal-risk equations using D flip-flops
    so J-K flip-flops didn’t save us anything

## Slide 43: Case 3: Synthesis Using JK FF
  Minimal cost using JK FF
J1 =1,
K1 = 0
J2 = Q1.Q3¢.A¢ + Q3.A
K2 = Q3¢.A.B¢ + Q3.A¢.B¢
J3 =A
K3 = A¢

## Slide 44: Case 3: Synthesis Using JK FF
  This circuit has two more gates than the minimal-cost D circuit
    J-K flip-flops still didn’t save us anything.

## Slide 45: Sequential Circuit Design Using ROM or PLA
 |  |  |  |  |  | Z | 
 | Q1 | Q2 | Q3 | X=0 | X=1 | X=0 | X=1
A B C D E H K | 0 0 0 0 1 1 1 | 0 0 1 1 0 0 1 | 0 1 0 1 0 1 0 | 001 011 100 101 101 000 000 | 010 100 100 101 110 000 - | 1 1 0 0 1 0 1 | 0 0 1 1 0 1 -

## Slide 46: Sequential Circuit Design Using ROM or PLA
X | Q1 | Q2 | Q3 | Z | D1 | D2 | D3
0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 | 0 0 0 0 1 1 1 1 0 0 0 0 1 1 1 1 | 0 0 1 1 0 0 1 1 0 0 1 1 0 0 1 1 | 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 | 1 1 0 0 1 0 1 x 0 0 1 1 0 1 x x | 0 0 1 1 1 0 0 x 0 1 1 1 1 0 x x | 0 1 0 0 0 0 0 x 1 0 0 0 1 0 x x | 1 1 0 1 1 0 0 x 0 0 0 1 0 0 x x
*ROM OUTPUTS (Z,D1,D2 and D3)
*ROM INPUTS
(X,Q1,Q3 and Q3)

## Slide 47: Sequential Circuit Design Using ROM
A ROM with four inputs (24 words) and four outputs is required.

## Slide 48: Sequential Circuit Design Using PLA
Segment of Sequential PAL